## Slide 1: Smoke Tools and Information for Prescribed Fire and Wildfire
Susan O’Neill, AirFire Team
USDA Forest Service, PNW Research Station
Photo – Ted Grussing

## Slide 2: Overview
Smoke Forecasting Systems
  Details of the BlueSky Smoke Modeling Framework
  Others: NOAA, HRRR-Smoke, AIRPACT, Canada Firework, Canada BlueSky
Monitoring Data Tool
Satellite Data
Wildland Fire Air Quality Response Program (WFAQRP) and Air Resource Advisors (ARA’s)
Do your own Smoke Modeling

## Slide 3: Smoke Forecasting Systems
BlueSky Daily Operational Runs http://www.airfire.org/data/bluesky-daily/
AIRPACT – Northwest US http://lar.wsu.edu/airpact/
High Resolution Rapid Refresh (HRRR) – Smoke https://rapidrefresh.noaa.gov/hrrr/HRRRsmoke/
NOAA Air Quality http://www.nws.noaa.gov/airquality/ww.shtml
Firework – Canada https://weather.gc.ca/firework/index_e.html
BlueSky – Canada http://firesmoke.ca/
“Picking a model of choice for the day is a little like speed-dating: too little time/information to make up the mind leading to regrets by the end of the date/shift.”
- Wes Adkins, Meteorologist, National Weather Service, Juneau, AK
Notes: Links in Lesson Plan

## Slide 4: BlueSky Smoke Modeling Framework Components to Calculating Fire Emissions
Fire Info
Fuels
Total Consumption
Time Rate
Emissions
Plume Rise
Smoke Modeling
SMARTFIRE2 NOAA HMS
GEOMAC
IRWIN
Rx Sys
Manual
Other
FCCS
FCCS-LF
NFDRS
Hardy
GVDS LANDFIRE Ag
Other
CONSUME
FOFEM FEPS
FLAMBE
FINN
Other
Rx / WF
FEPS FOFEM
EPM WRAP Other
FEPS Literature EPM FOFEM
FLAMBE
FINN Other
Briggs
FRP
Other
HYSPLIT,
CMAQ, VSMOKE
GEM-MACH
Meteorology
WRF
MM5
NARR
Station data

## Slide 5
Fire Info
Fuels
Total Consumption
Time Rate
Emissions
Plume Rise
Smoke Modeling
Large uncertainties exist with each modeling step
Meteorology

## Slide 6
Fire Info
Fuels
Total Consumption
Time Rate
Emissions
Plume Rise
Dispersion /
Trajectories
Fire Info
Fuels
Total Consumption
Time Rate
Emissions
Plume Rise
Dispersion /
Trajectories
Reality
Reality
right answer, wrong reasons
right answer, right reasons

## Slide 7: Tailored Smoke Predictions Delivered to Incident Management Teams
Domains
  2-km CA/NV
  6-km Western US
  1.33-km WA/ID
  4-km PNW
  12-km CONUS
  12-km Alaska
  3-km CONUS
  1.8-km AZ/NM
  1-km FW (moveable)
Partnerships: NWS, UW, DRI, UofA
HYSPLIT – Primary near-surface 1-hr PM2.5
Notes: Partnerships!

## Slide 8: Tailored Smoke Predictions Delivered to Incident Management Teams
Fire Activity Information
NOAA Hazard Mapping System (HMS) Satellite Fire Detections
SmartFire v2 (SF2) augments (fire type, fire size, aggregation)
Notes: Partnerships!

## Slide 9: Tools for Wildfire and Rx Fire Smoke https://tools.airfire.org/

## Slide 10
http://www.airfire.org/data/bluesky-daily/
Successful!
Running (click on “view logs” for run progress)
Number of Fires
Website shows status of current runs
Failures show up in red.
Notes: 12 domains per day, 6 are run twice a day (00Z, 12Z) – 18 hysplit particle runs. Many puff runs too.
This does not include custom runs.

## Slide 11: Daily BlueSky Production Runs 12/10/2017 Satellite Fire Detections & PM2.5, 6-km http://www.airfire.org/data/bluesky-daily/

## Slide 12: AIRPACT – Northwest
CMAQ
4-km
72-hours
Ozone, PM2.5
BlueSky Fire Emissions

## Slide 13: NOAA HRRR-Smoke (High Resolution Rapid Refresh)
Coupled Meteorology/Smoke (WRF-Chem)
3-km, CONUS, Alaska
Primary PM2.5
Visible Infrared Imaging Radiometer Suite (VIIRS)
  fire activity
  fire radiative power (FRP)
Plume Rise – FRP
Emissions – FRP
00Z, 06Z, 12Z, 18Z
36-hrs
https://rapidrefresh.noaa.gov/hrrr/HRRRsmoke/

## Slide 14: HRRR-Smoke Near-Surface PM2.5

## Slide 15: HRRR-Smoke Vertically Integrated PM2.5

## Slide 16: National Weather Service
HYSPLIT
CMAQ
Ozone, PM2.5
12-km
84-hours
BlueSky Fire Emissions

## Slide 17: National Weather Service Fire Weather 1.27-km Domains
00Z, 06Z, 12Z, 18Z
36-hr
Custom BlueSky Runs - 2-hr setup
Meteorological Products available with the NWS 1km Domains
  http://www.emc.ncep.noaa.gov/mmb/mmbpll/firewx/

## Slide 18: Firework – Canada
GEM-MACH
10-km
48-hrs
PM2.5 from only fires
CWFIS – Canadian Emissions
BlueSky – US Emissions
North America
Notes: GEM-MACH Air Quality Model
00Z, 12Z
Using CWFIS and BlueSky for fire emissions
Ozone too, but that is not publically available

## Slide 19: BlueSky Canada
BlueSky – Emissions and HYSPLIT
4-km, 12-km
48-hrs
CWFIS – Canadian Emissions
PM2.5 from fires
Notes: 12km national,
4km – west and east
HYSPLIT puff mode
00Z, 12Z

## Slide 20: Smoke Monitoring Tool (Permanent and Temporary Monitors) https://tools.airfire.org/

## Slide 21: Monitoring Data Tool – Real-time PM2.5 Permanent and Temporary Monitors
https://tools.airfire.org/
Notes: Data as of 20171210 8am PST

## Slide 22: Monitoring Data Tool – Real-time PM2.5 Permanent and Temporary Monitors
https://tools.airfire.org/
Notes: Data as of 20171210 8am PST

## Slide 23: Monitoring Data Tool – Real-time PM2.5 Permanent and Temporary Monitors
https://tools.airfire.org/
Notes: Data as of 20171210 8am PST

## Slide 24: Monitoring Data Tool – Real-time PM2.5 Permanent and Temporary Monitors
https://tools.airfire.org/
Notes: Data as of 20171210 8am PST

## Slide 25: Satellite Information
Infusing Satellite Data into Environmental Applications (IDEAS) https://www.star.nesdis.noaa.gov/smcd/spb/aq/
Enhanced Infusing Satellite Data into Environmental Applications (eIDEAS) https://www.star.nesdis.noaa.gov/smcd/spb/aq/eidea/index.php
GOES-16 http://rammb-slider.cira.colostate.edu/
NASA Worldview https://worldview.earthdata.nasa.gov/
Stay tuned for more
  GOES-16 Launched 11/2016 – in GOES East Position
  NOAA-20 Launched 11/18/2017
  GOES-S Launched 03/2018 – will be GOES-17 in GOES-West Position
Notes: eIDEAS training video: https://www.youtube.com/watch?v=ctaLtcbJ6YY&feature=youtu.be

## Slide 26: NASA WORLDVIEW

## Slide 27: GOES-16 9/4/2017 14:12 PDT

## Slide 28: GOES-16 9/4/2017 14:12 PDT

## Slide 29: Enhanced Infusing Satellite Data for Environmental Applications (eIDEAS)

## Slide 30
Notes: TODO: get GOES-16, do a CANSAC-2km analysis, 2017090300, 2017090312, 2017090400

## Slide 31: 9/4/2017 13:00 PDT
BlueSky
Global Forecast System (GFS)
Column Average

## Slide 32: Putting on Your Smoke Glasses

## Slide 33: Carlton Complex Washington State 2014 250,000 acres
http://en.wikipedia.org/wiki/2014_Washington_state_wildfires
Notes: Use this example to talk about: grid resolution, comparing with monitoring data, timing of impacts and met models being off, calibrating your brain/experience
Example of: our production runs, how they get used by the ARA program for wildfires

## Slide 34: Carlton Complex August 2014
Washington Smoke Blog On this gorgeous, clear day with no smoke, let's take a look at the differences between two air quality monitors located less than 9 miles apart in the same Methow Valley. The blue graphs indicate 1-hr average concentrations of PM2.5 while the red data points are 24-hr averages. Note that while the 24-hr values trended rather similar for the two sites (expected as they are spatially close) the peak 1-hr values differed greatly!
Posted by Mike Broughton, FWS, ARA
Notes: Read the smoke blog to the class, then say, lets take it a step further and look at the models.
http://www.wasmoke.blogspot.com/search?updated-max=2014-08-18T11:08:00-07:00&max-results=8&start=4&by-date=false
Talk about 1-hr and 24-hr concentrations. NAAQS are a 24-hr std. Does smoke stay the same over a 24-hr period? Why or why not?
Use this example to talk about: grid resolution, comparing with monitoring data, timing of impacts and met models being off, calibrating your brain/experience
http://kcts9.org/programs/in-close/environment/wildfires-and-climate-change
http://kcts9.org/programs/in-close/environment/carlton-complex-progression-map

## Slide 35: Carlton Complex, 8/4/2014 6am, 1.33 km Domain
Winthrop
Twisp
Notes: Meteorology – what if it is off by 30 degrees?
The obs showed Twisp getting hit harder, yet BlueSky typically hit Winthrop harder – work in process

## Slide 36: Carlton Complex, 8/4/2014 6am, 12 km Domain
Winthrop
Twisp
Notes: Meteorology – what if it is off by 30 degrees? Does it matter so much with this resolution?

## Slide 37: http://www.wildlandfiresmoke.net/
Air Resource Advisors
Deployed to Incident Management Teams & Geographic Area Commands
Modeling, Monitoring, Messaging
Smoke Monitoring Cache: 20 E-Samplers 6 EBAMS Carbon Monoxide
Trainings: 2013 – 2017
Pete Lahm, USFS WO, Coordinator
Notes: Screen dump of deployments
Add 2017 bar

## Slide 38: Air Resource Advisors
Notes: burnouts

## Slide 39: Smoke Outlooks
Smoke outlook for next 2 days
1-2 pages
Aimed for public dissemination/posting:
Smokeblogs
Public Meetings
Public bulletin boards
AQ/Health agencies email lists & daily coordination calls

## Slide 40: Smoke Blogs
http://wasmoke.blogspot.com/
http://oregonsmoke.blogspot.com/
http://californiasmokeinfo.blogspot.com/
http://idsmoke.blogspot.com/
Figure: Janice Peterson
Notes: WA (from Janice): Max day was 144,000+ And we're over 2.2 million lifetime views.

## Slide 41: BlueSky Playground Do your own Smoke Modeling
https://tools.airfire.org

## Slide 42
HYSPLIT Trajectories
Parcel of Air Travels in the Wind Field
Same Trajectory for a 50 acre burn as a 500 acre burn
Simulate Effect of Plume Rise
Spot Weather Forecasts
https://ready.arl.noaa.gov/HYSPLIT.php

## Slide 43: HYSPLIT Trajectory Example

## Slide 44: Thank you!
US Forest Service, F&AM, FERA
National Park Service
National Weather Service
Environmental Protection Agency
Environment and Climate Change Canada
Joint Fire Science Program
NASA
University of Washington
Desert Research Institute
University of Arizona
many others
Susan O’Neill
smoneill@fs.fed.us
206-732-7851